DIVISION OF FACILITIES DEVELOPMENT

BUILDING DATA/COST REPORT - INSTRUCTIONS FOR COMPLETION

BUILDING DATA

Type of Construction:  Identify the type of construction classification per Wis. Adm. Code 51.03

Fire Protected - (Includes Wisconsin Code Types 1, 2 & 3)  Either fire protected structural steel or reinforced concrete frame; poured in place or precast concrete floors and roof deck; masonry, precast, or metal and glass curtain wall.

Ordinary (Unprotected) - (Includes Wisconsin Code Types 4 & 5) Masonry load bearing walls with unprotected steel or wood floor framing; wood or steel joists or trusses; metal or wood roof deck.

Frame - (Includes Wisconsin Code Types 6, 7 & 8) Either wood or metal studs with wood or steel interior columns; wood floor and roof framing.  Characterized by combustible materials.

Engineered Metal - Unprotected prefabricated metal building systems with exterior covering of prefabricated panels or sheet metal siding.  Characterized by non-combustible construction (Wisconsin Code Type 6).

Pole - Wood poles used both to form foundation and to support the roof; wood joists or trusses; non-combustible cladding (Wisconsin Code Type 6).

Gross Square Feet:  The sum of the enclosed areas on all floors of the building.  This to include basements, mezzanine and intermediate floored tiers and penthouses of headroom height, measured from the exterior faces of exterior walls or from the center line of walls separating buildings.  The gross area does include stairwells, elevator shafts and mechanical chases, but not include such features as pipe trenches, exterior terraces or steps, chimneys, pilasters, etc.

Assignable Square Feet:  The sum of areas on all floors, assigned to or available for assignment to an occupant or program function.  Assignable areas shall be the sum of all enclosed assignable spaces, measured from the inside faces of the walls.  Unfinished space is included.  Areas not to be included as assignable space are, public circulation elements, custodial, mechanical, public restrooms, and building construction components (walls, columns, etc.).

Number Floors Below Grade:  The total number of floors with more than 50% of wall area below grade.

Number Floors Above Grade:  The total number of floors with more than 50% of wall area above grade, excluding penthouses.

Cubic Feet Building Volume: The total enclosed cubic content measured from the outside face of exterior walls and from the underside of the lowest floor construction to the average height of the finished roof surface.

User Capacity: The total number of design use units according to building type (No. beds, No. occupants, No. work stations, No. seats, No. residents, etc.).

Square Feet Developed Site Area:  The total developed area within the construction limits minus the area of the building measured to the outside face of foundations at grade level.

Square Feet Roof Area:  The gross area of roof measured horizontally from outer extent of overhang or outside face of parapet, including skylight, canopy, and plaza areas.

Number Elevator Stops:  The total number of stops for all passenger and freight elevators.

Number Plumbing Fixtures:  The total number of plumbing fixtures, including water closets, lavatories, showers, urinals, drinking fountains, utility sinks, but excluding roof drains, floor drains, and exterior hose bibbs.

MBH Heating Capacity:  Rated capacity of the heating equipment measured in thousands of Btu's per hour (3,412 Btu/kWh).

MBH Cooling Capacity:  Rated capacity of the cooling equipment measured in thousands of Btu's per hour (12,000 Btu/ton).

Square Feet Fire Protection:  The total floor area protected by automatic sprinklers or chemical fire suppression systems.

KVA Electrical Capacity:  The total rated capacity of the transformers or main switch (KVA = service amps x volts/1000).  Multiply result by 1.73 for three phase.

Construction Complete (Date):  Date of substantial completion.

BUDGET DATA

General Construction:  Includes amount of all general construction work excluding site work.  Based on the contractor's cost breakdown, the amount for each Division of work shall be assigned as follows:

Structure -	All building excavation, foundations, substructure, superstructure, fireproofing, etc.

Envelope  -	All exterior walls, roofing and waterproofing, insulation, miscellaneous metals, exterior doors, windows, etc.

Interior  -	All interior partitions, ceilings, flooring, mill work, hardware, fixed equipment, finishes, etc.

General

Conditions-	Performance bond, site overhead, etc.

Elevators - 	Includes amount for all elevators and conveying systems.

Special Construction and Equipment:  Includes the total amount for special construction such as environmental rooms, lab equipment, etc.

Mechanical Work:  Includes the total amount of all mechanical work excluding site utilities and utility services.  The mechanical work generally consists of the following separate contracts.

Plumbing		-	All building plumbing work.

HVAC	-	All building heating, ventilation, and air conditioning work.

Fire Protection	-	All automatic sprinkler or chemical fire suppression systems.

Test & Balance	-	All mechanical system testing and balancing work.

Miscellaneous

Mechanical Systems -	Refrigeration systems, energy management system, etc.

Electrical:

Power/Lighting - Includes amount of all electrical work excluding site lighting, service to the building, Audio/Visual, Voice/Data, Fire Alarm/Security, and Emergency Power.

Audio/Visual – Includes all system components within the building, from the point of initial external attachment to the building.

Voice/Data – Includes all system components within the building, from the point of initial external attachment to the building.

Fire Alarm/Security – Includes all system components within the building, from the point of initial external attachment to the building.

Emergency Power – Includes all system components within the building, from the point of initial external attachment.

Total Building Cost:  Total of all amounts related to building construction identified above.

Sitework:  Includes the total amount for all sitework either bid separate or part of other contracts.

Site Preparation-	All demolition, site grading, etc.

Site Development-	All paving, retaining walls, landscaping, etc.

Site Utilities  -	All utility service extensions from 5 ft. outside building, site utilities, site lighting, etc.

Total Construction Cost:  Total Building Cost, plus sitework cost.