## Slide 1: Changes to the WI Platting Law
2013 WI ACT 272
2013 WI ACT 280
2013 WI ACT 358

## Slide 2: Changes to the WI Platting Law Land Surveyor
Old law:
  Surveys and plats/maps done by
“Licensed Land Surveyor” and/or “Registered Land Surveyor”

## Slide 3: Changes to the WI Platting Law Land Surveyor
New law:
“Professional Land Surveyor”
  “Licensed Land Surveyor” and “Registered Land Surveyor” have been replaced throughout Ch. 236.
    Effective 8/1/14

## Slide 4: Changes to the WI Platting Law Plat Submittals
Old law:
Two submittal processes outlined in the statute
  Clerks submittal process
  Surveyors submittal process

## Slide 5: Changes to the WI Platting Law Plat Submittals
New law:
Submittal process streamlined into single process
Reflects the process currently being used
Electronic submittals allowed by statute
    Effective 8/1/14

## Slide 6: Changes to the WI Platting Law Plat Submittals
New law:
Surveyor submits plat to Plat Review and any approving authorities
Plat Review submits plat to any objecting review authorities
Plat Review makes the record document and certifies on behalf of all objecting authorities
Surveyor presents certified plat to approving authorities for final approval and signature
Signed plat is filed/recorded with Register of Deeds
    Effective 8/1/14

## Slide 7: Changes to the WI Platting Law Plat Submittals
Review of existing law:
Review time limits remain the same
Approving authorities have 90 days for preliminary plats; 60 days for final plats
Objecting authorities have 20 days
Plat Review has 30 days

## Slide 8: Changes to the WI Platting Law Plat Submittals
Review of existing law:
Final plats, submitted within 36 months, that ‘substantially conform’ to the preliminary plat are entitled to approval
Approving authorities can permit final plats that are a portion of the preliminary plat (phased developments)

## Slide 9: Changes to the WI Platting Law Plat Submittals
Review of existing law:
Approval is based upon any ordinance that is in effect when the subdivider submits a preliminary plat, or final plat if no preliminary plat is submitted
Approving authorities can require the subdivider to install public improvements and to provide security to insure that the installation is completed

## Slide 10: Changes to the WI Platting Law Security for Improvements
Old law:
Approving authorities could require a surety bond or other acceptable security
Improvements are made within a reasonable time
A specified portion of the cost of improvements shall be paid in advance

## Slide 11: Changes to the WI Platting Law Security for Improvements
New law:
The subdivider decides if security will be a performance bond or letter of credit
The amount of security shall be not more than 120% of the estimated total cost of improvements
Security may not be required for more than 14 months after the improvements are “substantially completed”
    Effective 8/1/14

## Slide 12: Changes to the WI Platting Law Security for Improvements
New law:
Thereafter, any withheld security may not be more than the cost to finish the remaining improvements plus 10% of the total cost of the completed improvements
This applies to all plats as of 8/1/14, even if plats were submitted for review prior to 8/1/14
    Effective 8/1/14

## Slide 13: Changes to the WI Platting Law Security for Improvements
New law:
“Substantially complete” is the time the binder coat is installed on streets/roads
If improvements are not streets/roads then when 90% of the public improvements ‘by cost’ are completed
    Effective 8/1/14

## Slide 14: Changes to the WI Platting Law Final Plats
Old law:
Margins for recordable document were 1 ½” binding margin of the left, 1” margins on remaining sides

## Slide 15: Changes to the WI Platting Law Final Plats
New law:
Plats shall have 1” margins on all sides
    Effective 8/1/14

## Slide 16: Changes to the WI Platting Law Final Plats
Old law:
All land dedicated to the public, except roads and streets shall be clearly labeled “Dedicated to the Public”

## Slide 17: Changes to the WI Platting Law Final Plats
New law:
All lands dedicated to the public shall be clearly labeled “Dedicated to the Public”
    Effective 8/1/14

## Slide 18: Changes to the WI Platting Law Final Plats
Old law:
Description of land in the Surveyor’s Certificate
  By metes and bounds, commencing from an original government corner……; or
  If land is located in a record subdivision or a recorded addition thereto, the land shall be described by the lot number, block and subdivision name previously tied to a corner of the PLSS

## Slide 19: Changes to the WI Platting Law Final Plats
New law:
Description of land in the Surveyor’s Certificate
  By metes and bounds, commencing from an original government corner…..; or
  If land is located in a record subdivision or a recorded addition thereto, or recorded certified survey map that has been previously tied to the monumented line of a ¼ section, GL, PC …and shall be described by lot, block, subdivision name or CSM number
    Effective 8/1/14

## Slide 20: Changes to the WI Platting Law Final Plats
Old law:
Recording a plat
  Contains a permanent nonfading black image on durable white media
  Media is 22 inches wide by 30 inches long
  Complies with s. 59.43 (2m)(b)4., Wis. Stats.
  Bears the Departments certification of no objection

## Slide 21: Changes to the WI Platting Law Final Plats
New law:
Recording a plat
  Contains a permanent nonfading black image on durable white media or on other media that is acceptable to the Register of Deeds
  Media is 22 inches wide by 30 inches long
  Complies with s. 59.43 (2m)(b)4., Wis. Stats.
  Bears the Departments certification of no objection
    Effective 8/1/14

## Slide 22: Changes to the WI Platting Law Final Plats
Review of existing law:
Recording time limits for a plat
  Plat must be recorded within 12 months of the last approval; and within 36 months of the first approval
  The plat contains all of the signed certificates and affidavits required by s. 236.12(3) & 236.21
  Recording time limits begin when approval certificates are signed on the recordable document

## Slide 23: Changes to the WI Platting Law Water
Old law:
“Lake and Stream Shore Plats”
Dedicated public access shall extend to the low water mark
Public access established per Ch. 236 may only be vacated by circuit court action
Land lying between the meander line and the waters edge shall be included within the lots/outlots on the plat
Location of ordinary high water mark not addressed

## Slide 24: Changes to the WI Platting Law Water
New law:
“Lake and Navigable Stream Shore Plats..”
Dedicated public access shall extend to the waters edge
Public access established per Ch. 236 may be vacated by circuit court action –or– may be discontinued under s. 66.1003 & 66.1006
    Effective 8/1/14

## Slide 25: Changes to the WI Platting Law Water
New law:
Land lying between the meander line and the waters edge shall be included within the lots/outlots on the plat and certified survey map
Water elevations at the date of the survey and the approximate high water elevation must be shown on the final plat
    Effective 8/1/14

## Slide 26: Changes to the WI Platting Law Water
New law:
“Ordinary high water marks” for monumentation and meander lines. Surveyors may:
Show an ordinary high water mark on plat/map that has been determined by the DNR or otherwise determined pursuant to law
Approximate the ordinary high water mark and show its location on the plat/map
    Effective 8/1/14

## Slide 27: Changes to the WI Platting Law Water
New law:
“Approximated ordinary high water marks”
“The location of the approximate ordinary high water mark shall be the point on the bank of a navigable stream or on the shore of a lake up to which the presence and action of surface water is so continuous as to leave a distinctive mark by erosion, destruction of terrestrial vegetation, or other easily recognized characteristics.”
    Effective 8/1/14

## Slide 28: Changes to the WI Platting Law Water
New law:
“Approximated ordinary high water marks”
“For purposes of this section, a map, plat, or survey that shows an approximate ordinary high water mark shall state on its face that the mark is shown for reference only.”
    Effective 8/1/14

## Slide 29: Changes to the WI Platting Law Water
New law:
“Public Trust Information”
A subdivision plat or a CSM that includes lots/outlots that extend to the waters edge per s. 236.16(4) shall show on its face the following statement:
"Any land below the ordinary high water mark of a lake or a navigable stream is subject to the public trust in navigable waters that is established under article IX, section 1, of the state constitution."
    Effective 8/1/14

## Slide 30: Changes to the WI Platting Law Water
Review of existing law:
A 60’ public access to the water’s edge, connected to existing public roads, at not more than ½ mile intervals is required; unless
Wider access at greater intervals is agreed upon by DNR and DOA

## Slide 31: Changes to the WI Platting Law Certified Survey Maps
Old law:
CSMs contain up to 4 parcels of land consisting of lots and outlots
All corners of the CSM shall be monumented
A CSM may be used to dedicate streets and other public areas when Owners’ and Mortgagees’ Certificates are included and the CSM is approved by the local unit of government

## Slide 32: Changes to the WI Platting Law Certified Survey Maps
Old law:
Description of land in the Surveyor’s Certificate
  By metes and bounds, commencing from an original government corner……; or
  If land is located in a record subdivision or a recorded addition thereto, the land shall be described by the lot number, block and subdivision name previously tied to a corner of the PLSS
No vacation process

## Slide 33: Changes to the WI Platting Law Certified Survey Maps
New law:
Monuments that fall within a street, the monument shall be placed at the side line/right of way
CSMs may be used to dedicate streets, public areas, and may grant easements to the public or any person, society, or corporation when Owners’ and Mortgagees’ Certificates are included and the CSM is approved by the local unit of government
Recording time limits are 12 months from last approval; 36 months from the first approval
    Effective 8/1/14

## Slide 34: Changes to the WI Platting Law Certified Survey Maps
New law:
Description of land in the Surveyor’s Certificate
  By metes and bounds, commencing from an original government corner…..; or
  If land is located in a record subdivision or a recorded addition thereto, or recorded certified survey map that has been previously tied to the monumented line of a ¼ section, GL, PC …and shall be described by lot, block, subdivision name or CSM number
    Effective 8/1/14

## Slide 35: Changes to the WI Platting Law Certified Survey Maps
New law:
Circuit court vacation
A CSM, or part of a CSM, may be vacated by the circuit court. The application may be made by:
The owner of any lot or outlot in the land that is the subject of the CSM
The county board if the county has acquired an interest by tax deed
    Effective 8/1/14

## Slide 36: Changes to the WI Platting Law Certified Survey Maps
New law:
Expanded use of CSMs
A local unit of government may allow more than 4 parcels on a CSM when:
They have an established planning agency;
A ordinance is enacted or resolution is passed;
A maximum number of parcels is specified; and
Land is zoned commercial, industrial or mixed use
    Effective 4/18/14

## Slide 37: Changes to the WI Platting Law Certified Survey Maps
New law:
Expanded use of CSMs
Requirements for passing an ordinance/resolution:
Receive recommendation from planning agency
Hold a public hearing noticed by publishing a class two notice
Enacted ordinance/resolution shall be published in a form suitable for public distribution
    Effective 4/18/14

## Slide 38: Changes to the WI Platting Law Certified Survey Maps
New law:
Expanded use of CSMs
Such enacted ordinance/resolution by a city or village may be applied to the extraterritorial plat approval jurisdiction area
When local units of government have conflicting requirements for these CSMs, the most restrictive requirements apply
    Effective 4/18/14

## Slide 39: Changes to the WI Platting Law Certified Survey Maps
New law:
Review of Expanded CSMs
Expanded CSMs that reconfigure lots/outlots within a record plat, assessors plat or CSM, where no additional parcels are created – are NOT reviewed by DOA
Expanded CSMs that create additional lots, in or out of a plat or map, ARE submitted to DOA for review (20 day review period; $100 per map)
    Effective 4/18/14

## Slide 40: Changes to the WI Platting Law Certified Survey Maps
New law:
Review of Expanded CSMs
Expanded CSMs that abut a state highway or connecting highway and change the exterior boundary of a plat or CSM must be submitted to DOT for review
Expanded CSMs that are located in the City of Milwaukee are not subject to state review
    Effective 4/18/14

## Slide 41
Plat Review
101 E. Wilson St. 9th FL
Madison, WI 53703
(608) 266-3200
Plat.Review@wi.gov
http://doa.wi.gov/platreview